VIII.	Appendix

Figure 1. A model of the one-hole system with no inflow of water.

| Pipe | R | r | h0 | f |
| --- | --- | --- | --- | --- |
| BB | 1” | 0.25” | 55.25” | 4” |
| BS | 1” | 0.125” | 58.6” | 3.3” |
| SB | 0.5” | 0.25” | 57.4” | 3.3” |
| SS | 0.5” | 0.125” | 55.7” | 3.25” |

Figure 2. Data on each of the four pipes used in the one-hole systems.  Note that the first letter in each pipe name refers to the pipe radius, and the second letter refers to the hole radius.  “B” stands for “big,” and “S” stands for “small.”

| Pipe | Trial 1 | Trial 2 | Trial 3 | Trial 4 | Trial 5 | Average | Theory | %Error |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| BB | 13.2 s | 13.3 s | 13.6 s | 13.2 s | 13.1 s | 13.3 s | 14.4 s | 7.6 % |
| BS | 50.6 s | 50.2 s | 50.2 s | 50.3 s | 50.5 s | 50.4 s | 59.4 s | 15.2 % |
| SB | 3.8 s | 3.8 s | 3.6 s | 3.7 s | 3.9 s | 3.8 s | 3.7 s | 2.7 % |
| SS | 13.2 s | 13.0 s | 13.2 s | 13.2 s | 13.1 s | 13.1 s | 14.5 s | 9.7% |

Figure 3. Data for Experiment 1.

Figure 4. The calculations involved in deriving the exit velocity.

| Pipe BB | Distance | Time | Velocity |
| --- | --- | --- | --- |
| Trial 1 | 0” | 13.30 s | 0 in/s |
| Trial 2 | 8” | 11.87 s | 26.2 in/s |
| Trial 3 | 16” | 10.37 s | 52.4 in/s |
| Trial 4 | 28” | 6.65 s | 91.7 in/s |
| Trial 5 | 40” | 4.04 s | 131.0 in/s |
| Trial 6 | 58” | 0 s | 189.9 in/s |
| Pipe BS | Distance | Time | Velocity |
| Trial 1 | 0” | 50.40 s | 0 in/s |
| Trial 2 | 8” | 45.54 s | 26.7 in/s |
| Trial 3 | 16” | 39.12 s | 53.4 in/s |
| Trial 4 | 28” | 28.93 s | 93.5 in/s |
| Trial 5 | 40” | 22.70 s | 133.6 in/s |
| Trial 6 | 62” | 0 s | 207.1 in/s |
| Pipe SB | Distance | Time | Velocity |
| Trial 1 | 0” | 3.80 s | 0 in/s |
| Trial 2 | 8” | 3.31 s | 26.7 in/s |
| Trial 3 | 16” | 3.04 s | 53.4 in/s |
| Trial 4 | 28” | 2.04 s | 93.5 in/s |
| Trial 5 | 40” | 1.01 s | 133.6 in/s |
| Trial 6 | 60” | 0 s | 200.4 in/s |
| Pipe SS | Distance | Time | Velocity |
| Trial 1 | 0” | 13.1 s | 0 in/s |
| Trial 2 | 8” | 12.1 s | 26.8 in/s |
| Trial 3 | 16” | 10.4 s | 53.5 in/s |
| Trial 4 | 28” | 6.89 s | 93.7 in/s |
| Trial 5 | 40” | 4.59 s | 133.8 in/s |
| Trial 6 | 58” | 0 s | 194.0 in/s |

(Note: The bucket height was 14 inches.)

Figure 5. The results of Experiment 2.

| hBB = 0.26598t^2 - 7.66689t + 55.25, t < 14.4126 | vBB = -8.51130t + 123.169 | VBB = 0.83559t^2 - 24.0862t + 173.573 |
| --- | --- | --- |
| hBS = 0.01662t^2 - 1.97398t + 58.6, t < 59.3726 | vBS = -2.12783t + 126.334 | VBS = 0.05222t^2 - 6.20143t + 184.097 |
| hSB = 4.25565t^2 - 31.2586t + 57.4, t < 3.67259 | vSB = -34.0452t + 125.034 | VSB = 3.34238t^2 - 24.5504t + 45.0819 |
| hSS = 0.26598t^2 - 7.69805t + 55.7, t < 14.4712 | vSS = -8.51130t + 123.169 | VSS = 0.20890t^2 - 6.04603t + 43.7467 |

Figure 6. Equations for the height, velocity, and volume for each of the four pipes.  The value for t in each entry in the first column indicates when all functions will fall to and remain at 0.

Figure 7. Graphs of the (respective) height, velocity, and volume of each pipe against time.  Pipe BB is green, pipe BS is red, Pipe SB is blue, and pipe BB is yellow.

Figure 8. Comparisons of the experimental and theoretical models for v(t).  In each graph, the model that goes below 0 is experimental, and the one that stays above is theoretical.  The graphs are only valid up to the point where v first hits 0.

Figure 9. Comparisons of the experimental and theoretical models for h(t), in the order BB, BS, SB, SS.  The red curve indicates the theoretical value, while the blue curve indicates the experimental value.

Figure 10. Visual models of Systems 2 through 4.

Figure 11. A slope field for System 2.  x refers to t and is in seconds.  y refers to h and is in inches.

| Trial 1 | Trial 2 | Trial 3 | Trial 4 | Trial 5 | Average |
| --- | --- | --- | --- | --- | --- |
| 42.9 s | 39.1 s | 43.5 s | 43.7 s | 44.1 s | 42.66 s |

t = 42.66 s

h0 = 53.96 in

Figure 12. The calculations involved in finding the experimental water column height.

Figure 13. A slope field for System 3.  y refers to h in inches, and x refers to t in seconds.

| Trial 1 Trial 2 Trial 3 Trial 4 Trial 5 Average 41.6 s 40.9 s 41.2 s 40.9 s 41.0 s 41.1 s Figure 14. The experimental draining time for System 3. Figure 15. A slope field for System 4. y refers to h in inches, and x refers to t in seconds. |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |